## Slide 1: Truck Assignment & Route Optimization for Cross‑Border Logistics
Mehmet Yusuf Demirci / 31187
Faculty of Engineering and Natural Sciences
Industrial Engineering
https://github.com/mhmtysfdmrc25/-Truck-Assignment-and-Route-Optimization-for-Cross-Border-Logistics-Using-Gurobi

## Slide 2: Business Problem & Corridor
Planning corridor: Istanbul → Kapıkule (TR–BG) → Strasbourg (FR entry) → French delivery cities → Kapıkule → Istanbul
Goal: Assign trucks and optimize routes to minimize total cost while satisfying all demands
Cost = Fixed per active truck + Fuel cost × total km (base legs + in‑France legs)
Respect truck capacity and ensure each French delivery node is visited exactly once

## Slide 3: Data & Inputs
Distance matrix: square Excel (rows==columns), file: 'distances matrix.xlsx'
Nodes: Origin (Istanbul), Transit (Kapıkule, Strasbourg), Deliveries in France (11 cities)
Demands: defined for French nodes (kg), transit nodes have zero demand
trucks: total 120 (planning up to 110 active). Capacity per truck ≈ 23,000 kg
Costs: Fixed €2,700 per active truck, Fuel ≈ €0.32/km

## Slide 4: Data Integrity & Sources
No. All the data determined with the operation team in VIP Lojistik.
The fixed cost includes the driver's progress payment (€920), invoices (€750), and road tolls.
These road tolls include:
Bulgarian toll: €55 one-way
Slovenian toll: €20 one-way
Austrian toll: €220 one-way
Germany toll: €220 one-way
These totals, as an average fixed cost for a truck, amount to €2700 (round trip). Additionally, the fuel cost per km was calculated as follows: a truck consumes 1000 liters of fuel for an average distance of 3200 km. Furthermore, I learned from operation team that, including tax refunds and their own discounts, logistics companies in Europe have an average fuel price of €1/liter. Therefore, the "km_cost" parameter used in the code was calculated and added to €0.32/km.
For distance matrix, I learned the locations and its demands from operation team and construct the distance matrix by hand getting the distances from Google Maps.

## Slide 5: Objective Function
Minimize
F = 2700 EUR/truck (fixed), α = 0.32 EUR/km (fuel), B = base‑legs distance (Istanbul↔ Kapıkule ↔ Strasbourg ↔ Kapıkule ↔ Istanbul)
= in‑France arc distances; decision vars select arcs; activates trucks
Constraints: coverage (no-split) or demand balance (split); capacity; flow; start/end; MTZ subtour

## Slide 6: Modeling Approaches
Variant A – Without Mixed Fleet (Split deliveries disabled)
• Baseline (No split deliveries): each city served by exactly one truck
• Classical VRP coverage: capacity & flow constraints; MTZ for subtours
• Implication: more trucks activated to respect capacity → fixed charges dominate

## Slide 7: Model Script — Code Snapshot
# 4) Parametreler
num_trucks = 110
truck_capacity = 23000 # kg (gümrük kanunlarına göre çeker+dorse max 40ton alabilir, 23ton ortalama araca eklenebilen mal)
fixed_cost = 2700 # € / truck (ortalama şoför, hakediş, otoyol masrafları vs.)
km_cost = 0.32 # € / km (tır başına ortalama benzin masrafı km başına, şirketlere özel indirimle birlikte, 3200km için 1000LT benzin ortalama 1€/lt'den)
distance = df.values.tolist()
# 5) Model Kurulumu
base_leg_km = (
distance[origin_index][end_index]
+ distance[end_index][start_index]
+ distance[end_index][origin_index]
)
# 5) Model
model = Model("TruckRoutingVRP")
# Ark kümesi (Strasbourg'dan başlar, Kapıkule'de biter)
arcs = [
(i, j)
for i in [start_index] + delivery_indexes
for j in delivery_indexes + [end_index]
if i != j
]
# y[t,i,j]: t tırı i -> j arkını kullanır
y = model.addVars(num_trucks, arcs, vtype=GRB.BINARY, name="y")
# z[t]: t tırı kullanıldı mı?
z = model.addVars(num_trucks, vtype=GRB.BINARY, name="z")
# x[t,j]: t tırı teslimat j'yi ziyaret etti mi?
x = model.addVars(num_trucks, delivery_indexes, vtype=GRB.BINARY, name="x")
CONTINUES..
# u[t,j]: MTZ sıra değişkeni
u = model.addVars(
num_trucks,
delivery_indexes,
lb=0,
ub=len(delivery_indexes),
vtype=GRB.CONTINUOUS,
name="u",
)
# Amaç: sabit + km maliyeti
model.setObjective(
quicksum(fixed_cost * z[t] for t in range(num_trucks))
+ km_cost
* (
quicksum(
distance[i][j] * y[t, i, j]
for t in range(num_trucks)
for i, j in arcs
)
+ base_leg_km * quicksum(z[t] for t in range(num_trucks))
),
GRB.MINIMIZE,
)

## Slide 8: Model Script — Code Snapshot
Core of the model:
Binary activation per truck
Customer assignment
In-France arc selection
MTZ order variables
The objective minimizes fixed truck costs (F) plus fuel cost α×km, where km includes the France arcs and the corridor base-legs Istanbul ↔ Kapıkule ↔ Strasbourg ↔ … (in France destinations) …↔ Kapıkule ↔ Istanbul

## Slide 9: Modeling Approaches
Variant B – With Mixed Fleet (Split Deliveries Enabled)
• Split deliveries enabled (order sharing across trucks) via load variables ≥ 0
• Demand balance: ≤ Q
• Implication: fewer trucks, higher load factors, lower total cost

## Slide 10: Model Script — Code Snapshot
# 4) Parametreler
num_trucks = 110
truck_capacity = 23000 # kg (gümrük kanunlarına göre çeker+dorse max 40ton alabilir, 23ton ortalama araca eklenebilen mal)
fixed_cost = 2700 # € / truck (ortalama şoför, hakediş, otoyol masrafları vs.)
km_cost = 0.32 # € / km (tır başına ortalama benzin masrafı km başına, şirketlere özel indirimle birlikte, 3200km için 1000LT benzin ortalama 1€/lt'den)
distance = df.values.tolist()
# demand per location (kg)
demand = {
lower.index("istanbul"): 0,
lower.index("lille"): 6351,
lower.index("macon"): 11580,
lower.index("colmar"): 8767,
lower.index("kapıkule"): 0,
lower.index("beauvais"): 14781,
lower.index("nantes"): 1900,
lower.index("strasbourg"): 0,
lower.index("rouen"): 22483,
lower.index("versailles"): 2139,
lower.index("goussainville"): 8095,
lower.index("saint michel sur orge"): 13218,
lower.index("orleans"): 10885,
lower.index("melun"): 3933,
}
# 6) Objective: fixed cost + travel cost
m.setObjective(
quicksum(fixed_cost * z[t] for t in range(num_trucks))
+ km_cost * (
quicksum(dist[i][j] * y[t, i, j] for t in range(num_trucks) for i, j in arcs)
+ base_leg_km * quicksum(z[t] for t in range(num_trucks))
),
GRB.MINIMIZE
)
# --- Demand is fully delivered (can be split)
for j in deliveries:
m.addConstr(quicksum(q[t, j] for t in range(num_trucks)) == demand[j],
name=f"demand_{j}")
# 5) Model Kurulumu
base_leg_km = (
distance[origin_index][end_index]
+ distance[end_index][start_index]
+ distance[end_index][origin_index]
)
# 5) Model
model = Model("TruckRoutingVRP")
# Ark kümesi (Strasbourg'dan başlar, Kapıkule'de biter)
arcs = [
(i, j)
for i in [start_index] + delivery_indexes
for j in delivery_indexes + [end_index]
if i != j
]
y = m.addVars(num_trucks, arcs, vtype=GRB.BINARY, name="y") # route
x = m.addVars(num_trucks, deliveries, vtype=GRB.BINARY, name="x") # visit
q = m.addVars(num_trucks, deliveries, lb=0.0, name="q") # delivered load
z = m.addVars(num_trucks, vtype=GRB.BINARY, name="z") # truck used
u = m.addVars(num_trucks, deliveries, lb=0.0,
ub=len(deliveries), name="u") # MTZ

## Slide 11: Model Script — Code Snapshot
Core of the model:
Decision variables
(truck-arc use), (truck visits city j), (delivered load), {0,1} (truck activated), (MTZ order).
Objective (minimize total cost)
min base_leg_km *
Demand fulfillment (split enabled)
for every delivery node j (cities can be served by multiple trucks).
Truck capacity
for each truck t (no load if the truck is not activated).
Load–visit linking
ensures positive delivered load only if truck t actually visits city j.
Flow/degree consistency
For any visited city j and truck t:
(enter = leave = visit).
Start/end activation on the corridor
and (each active truck departs Strasbourg and terminates at Kapıkule once).
Subtour elimination (per truck, MTZ)
Standard MTZ constraints on to prevent disconnected cycles.
At-least-one visit per city (when useful)
1 so each demand node is on at least one route (while the load itself may be split).
Corridor accounting
The constant corridor legs Istanbul→Kapıkule→Strasbourg→Istanbul are folded into base_leg_km * in the objective (a per-activated-truck cost term).

## Slide 12: Modeling Approaches
Variant C – With Mixed Fleet (Split deliveries enabled with extra demand)
• Purpose: real-company demands sometimes didn’t force sharing (each city fit in one truck)
• Action: randomly increased demands to stress-test; ensures mixed-filo effect is visible
• Result: stronger cost reduction by minimizing additional truck activations under load

## Slide 13: Model Script — Code Snapshot
# 4) Parametreler
num_trucks = 110
truck_capacity = 23000 # kg (gümrük kanunlarına göre çeker+dorse max 40ton alabilir, 23ton ortalama araca eklenebilen mal)
fixed_cost = 2700 # € / truck (ortalama şoför, hakediş, otoyol masrafları vs.)
km_cost = 0.32 # € / km (tır başına ortalama benzin masrafı km başına, şirketlere özel indirimle birlikte, 3200km için 1000LT benzin ortalama 1€/lt'den)
distance = df.values.tolist()
# demand per location (kg)
demand = {
lower.index("istanbul"): 0,
lower.index("lille"): 16351,
lower.index("macon"): 21580,
lower.index("colmar"): 18767,
lower.index("kapıkule"): 0,
lower.index("beauvais"): 24781,
lower.index("nantes"): 11900,
lower.index("strasbourg"): 0,
lower.index("rouen"): 32483,
lower.index("versailles"): 12139,
lower.index("goussainville"): 18095,
lower.index("saint michel sur orge"): 13218,
lower.index("orleans"): 10885,
lower.index("melun"): 3933,
}
# 6) Objective: fixed cost + travel cost
m.setObjective(
quicksum(fixed_cost * z[t] for t in range(num_trucks))
+ km_cost * (
quicksum(dist[i][j] * y[t, i, j] for t in range(num_trucks) for i, j in arcs)
+ base_leg_km * quicksum(z[t] for t in range(num_trucks))
),
GRB.MINIMIZE
)
# --- Demand is fully delivered (can be split)
for j in deliveries:
m.addConstr(quicksum(q[t, j] for t in range(num_trucks)) == demand[j],
name=f"demand_{j}")
# 5) Model Kurulumu
base_leg_km = (
distance[origin_index][end_index]
+ distance[end_index][start_index]
+ distance[end_index][origin_index]
)
# 5) Model
model = Model("TruckRoutingVRP")
# Ark kümesi (Strasbourg'dan başlar, Kapıkule'de biter)
arcs = [
(i, j)
for i in [start_index] + delivery_indexes
for j in delivery_indexes + [end_index]
if i != j
]
y = m.addVars(num_trucks, arcs, vtype=GRB.BINARY, name="y") # route
x = m.addVars(num_trucks, deliveries, vtype=GRB.BINARY, name="x") # visit
q = m.addVars(num_trucks, deliveries, lb=0.0, name="q") # delivered load
z = m.addVars(num_trucks, vtype=GRB.BINARY, name="z") # truck used
u = m.addVars(num_trucks, deliveries, lb=0.0,
ub=len(deliveries), name="u") # MTZ

## Slide 14: Model Script — Code Snapshot
Core of the model:
Same model structure as Variant B
Identical variables, objective, and constraints (split deliveries enabled).
Stress-test demand vector
City demands are increased (some exceeding Q) to force splitting and reveal the benefit of mixed-filo planning.
Feasibility under higher loads
The equality guarantees full service; when > Q, multiple trucks must share city j.
Capacity & activation trade-off
The model balances extra distance from additional visits against avoiding new truck activations (saving the fixed cost F €2700 per avoided truck).
Route structure effects
More cities get multi-truck visits (several ), yet total remains near the theoretical minimum thanks to higher load factors.
Cost behavior
Total cost > Variant B (because total demand is larger) but strictly lower than a no-split baseline at the same demand, due to better consolidation.
Corridor & MTZ unchanged
Start/end degree and MTZ subtour constraints remain as in Variant B; base_leg_km * still charges corridor legs per active truck.

## Slide 15: Why “Mixed Fleet (Splitting deliveries)” Reduces Cost?
Fixed-charge leverage: each avoided truck saves ~€2,700
Higher load factors: share orders to approach 23 tons utilization
Avoid awkward edges: near-capacity single-city demands no longer force a whole extra truck
Scales under stress: benefit grows as total demand rises or skews

## Slide 16: Stress Test — Extra Demand Rationale
Real demand sometimes let one truck serve a city, hiding split benefits
By increasing demands, the optimizer must split and consolidate intelligently
Outcome: a clear drop in activated trucks and total cost versus baseline

## Slide 17: Assumptions & Limitations
No time windows or driving hours; single-period planning (no driver-hour rules).
Fuel price is assumed constant; toll roads are included in the fixed cost by averaging.
Assuming there is only one way (only highway with trucks) to carry the goods.

## Slide 18: Future Work
Optimization of ship transportation or mixed ship & road transportation.
CO₂ emissions accounting
Optimization of volume of products while splitting them into trucks.

## Slide 19: References & Acknowledgments
Thanks: VIP Lojistik Fleet Operations for data & validation
Old course materials (ENS208, IE311, IE312 etc.)
Gurobi Optimizer

## Slide 20: Thank You